1c1
< # Generated by PNCconf at Mon Feb  1 10:04:16 2016
---
> # Generated by PNCconf at Thu May 31 17:23:15 2018
8c8
< loadrt hm2_pci config=" num_encoders=3 num_pwmgens=0 num_stepgens=0 sserial_port_0=000xxx" 
---
> loadrt hm2_pci config=" num_encoders=12 num_pwmgens=0 num_stepgens=0 sserial_port_0=000000" 
23a24,26
> # --- MACHINE-IS-ENABLED ---
> net machine-is-enabled hm2_5i25.0.7i77.0.3.output-00
> 
26a30,41
> # --- ESTOP-EXT ---
> net estop-ext     <=  hm2_5i25.0.7i77.0.3.input-00
> 
> # --- BOTH-X ---
> net both-x     <=  hm2_5i25.0.7i77.0.3.input-13
> 
> # --- BOTH-Y ---
> net both-y     <=  hm2_5i25.0.7i77.0.3.input-14
> 
> # --- BOTH-Z ---
> net both-z     <=  hm2_5i25.0.7i77.0.3.input-15
> 
41d55
< setp   pid.x.maxerror 0.0
52,54c66,68
< setp   hm2_5i25.0.7i77.0.1.analogout0-scalemax  [AXIS_0]OUTPUT_SCALE
< setp   hm2_5i25.0.7i77.0.1.analogout0-minlim    [AXIS_0]OUTPUT_MIN_LIMIT
< setp   hm2_5i25.0.7i77.0.1.analogout0-maxlim    [AXIS_0]OUTPUT_MAX_LIMIT
---
> setp   hm2_5i25.0.7i77.0.4.analogout0-scalemax  [AXIS_0]OUTPUT_SCALE
> setp   hm2_5i25.0.7i77.0.4.analogout0-minlim    [AXIS_0]OUTPUT_MIN_LIMIT
> setp   hm2_5i25.0.7i77.0.4.analogout0-maxlim    [AXIS_0]OUTPUT_MAX_LIMIT
56c70
< net x-output                             => hm2_5i25.0.7i77.0.1.analogout0
---
> net x-output                             => hm2_5i25.0.7i77.0.4.analogout0
60c74
< net x-enable   hm2_5i25.0.7i77.0.1.analogena
---
> net x-enable   hm2_5i25.0.7i77.0.4.analogena
64,69c78,83
< setp    hm2_5i25.0.encoder.00.counter-mode 0
< setp    hm2_5i25.0.encoder.00.filter 1
< setp    hm2_5i25.0.encoder.00.index-invert 0
< setp    hm2_5i25.0.encoder.00.index-mask 0
< setp    hm2_5i25.0.encoder.00.index-mask-invert 0
< setp    hm2_5i25.0.encoder.00.scale  [AXIS_0]ENCODER_SCALE
---
> setp    hm2_5i25.0.encoder.06.counter-mode 0
> setp    hm2_5i25.0.encoder.06.filter 1
> setp    hm2_5i25.0.encoder.06.index-invert 0
> setp    hm2_5i25.0.encoder.06.index-mask 0
> setp    hm2_5i25.0.encoder.06.index-mask-invert 0
> setp    hm2_5i25.0.encoder.06.scale  [AXIS_0]ENCODER_SCALE
71,72c85,86
< net x-pos-fb               <=  hm2_5i25.0.encoder.00.position
< net x-vel-fb               <=  hm2_5i25.0.encoder.00.velocity
---
> net x-pos-fb               <=  hm2_5i25.0.encoder.06.position
> net x-vel-fb               <=  hm2_5i25.0.encoder.06.velocity
74,75c88,89
< net x-index-enable    axis.0.index-enable  <=>  hm2_5i25.0.encoder.00.index-enable
< net x-pos-rawcounts        <=  hm2_5i25.0.encoder.00.rawcounts
---
> net x-index-enable    axis.0.index-enable  <=>  hm2_5i25.0.encoder.06.index-enable
> net x-pos-rawcounts        <=  hm2_5i25.0.encoder.06.rawcounts
80,81c94,95
< net x-neg-limit     =>  axis.0.neg-lim-sw-in
< net x-pos-limit     =>  axis.0.pos-lim-sw-in
---
> net both-x     =>  axis.0.neg-lim-sw-in
> net both-x     =>  axis.0.pos-lim-sw-in
97d110
< setp   pid.y.maxerror 0.0
108,110c121,123
< setp   hm2_5i25.0.7i77.0.1.analogout1-scalemax  [AXIS_1]OUTPUT_SCALE
< setp   hm2_5i25.0.7i77.0.1.analogout1-minlim    [AXIS_1]OUTPUT_MIN_LIMIT
< setp   hm2_5i25.0.7i77.0.1.analogout1-maxlim    [AXIS_1]OUTPUT_MAX_LIMIT
---
> setp   hm2_5i25.0.7i77.0.4.analogout1-scalemax  [AXIS_1]OUTPUT_SCALE
> setp   hm2_5i25.0.7i77.0.4.analogout1-minlim    [AXIS_1]OUTPUT_MIN_LIMIT
> setp   hm2_5i25.0.7i77.0.4.analogout1-maxlim    [AXIS_1]OUTPUT_MAX_LIMIT
112c125
< net y-output                             => hm2_5i25.0.7i77.0.1.analogout1
---
> net y-output                             => hm2_5i25.0.7i77.0.4.analogout1
118,123c131,136
< setp    hm2_5i25.0.encoder.01.counter-mode 0
< setp    hm2_5i25.0.encoder.01.filter 1
< setp    hm2_5i25.0.encoder.01.index-invert 0
< setp    hm2_5i25.0.encoder.01.index-mask 0
< setp    hm2_5i25.0.encoder.01.index-mask-invert 0
< setp    hm2_5i25.0.encoder.01.scale  [AXIS_1]ENCODER_SCALE
---
> setp    hm2_5i25.0.encoder.07.counter-mode 0
> setp    hm2_5i25.0.encoder.07.filter 1
> setp    hm2_5i25.0.encoder.07.index-invert 0
> setp    hm2_5i25.0.encoder.07.index-mask 0
> setp    hm2_5i25.0.encoder.07.index-mask-invert 0
> setp    hm2_5i25.0.encoder.07.scale  [AXIS_1]ENCODER_SCALE
125,126c138,139
< net y-pos-fb               <=  hm2_5i25.0.encoder.01.position
< net y-vel-fb               <=  hm2_5i25.0.encoder.01.velocity
---
> net y-pos-fb               <=  hm2_5i25.0.encoder.07.position
> net y-vel-fb               <=  hm2_5i25.0.encoder.07.velocity
128,129c141,142
< net y-index-enable    axis.1.index-enable  <=>  hm2_5i25.0.encoder.01.index-enable
< net y-pos-rawcounts        <=  hm2_5i25.0.encoder.01.rawcounts
---
> net y-index-enable    axis.1.index-enable  <=>  hm2_5i25.0.encoder.07.index-enable
> net y-pos-rawcounts        <=  hm2_5i25.0.encoder.07.rawcounts
134,135c147,148
< net y-neg-limit     =>  axis.1.neg-lim-sw-in
< net y-pos-limit     =>  axis.1.pos-lim-sw-in
---
> net both-y     =>  axis.1.neg-lim-sw-in
> net both-y     =>  axis.1.pos-lim-sw-in
151d163
< setp   pid.z.maxerror 0.0
162,164c174,176
< setp   hm2_5i25.0.7i77.0.1.analogout2-scalemax  [AXIS_2]OUTPUT_SCALE
< setp   hm2_5i25.0.7i77.0.1.analogout2-minlim    [AXIS_2]OUTPUT_MIN_LIMIT
< setp   hm2_5i25.0.7i77.0.1.analogout2-maxlim    [AXIS_2]OUTPUT_MAX_LIMIT
---
> setp   hm2_5i25.0.7i77.0.4.analogout2-scalemax  [AXIS_2]OUTPUT_SCALE
> setp   hm2_5i25.0.7i77.0.4.analogout2-minlim    [AXIS_2]OUTPUT_MIN_LIMIT
> setp   hm2_5i25.0.7i77.0.4.analogout2-maxlim    [AXIS_2]OUTPUT_MAX_LIMIT
166c178
< net z-output                             => hm2_5i25.0.7i77.0.1.analogout2
---
> net z-output                             => hm2_5i25.0.7i77.0.4.analogout2
172,177c184,189
< setp    hm2_5i25.0.encoder.02.counter-mode 0
< setp    hm2_5i25.0.encoder.02.filter 1
< setp    hm2_5i25.0.encoder.02.index-invert 0
< setp    hm2_5i25.0.encoder.02.index-mask 0
< setp    hm2_5i25.0.encoder.02.index-mask-invert 0
< setp    hm2_5i25.0.encoder.02.scale  [AXIS_2]ENCODER_SCALE
---
> setp    hm2_5i25.0.encoder.08.counter-mode 0
> setp    hm2_5i25.0.encoder.08.filter 1
> setp    hm2_5i25.0.encoder.08.index-invert 0
> setp    hm2_5i25.0.encoder.08.index-mask 0
> setp    hm2_5i25.0.encoder.08.index-mask-invert 0
> setp    hm2_5i25.0.encoder.08.scale  [AXIS_2]ENCODER_SCALE
179,180c191,192
< net z-pos-fb               <=  hm2_5i25.0.encoder.02.position
< net z-vel-fb               <=  hm2_5i25.0.encoder.02.velocity
---
> net z-pos-fb               <=  hm2_5i25.0.encoder.08.position
> net z-vel-fb               <=  hm2_5i25.0.encoder.08.velocity
182,183c194,195
< net z-index-enable    axis.2.index-enable  <=>  hm2_5i25.0.encoder.02.index-enable
< net z-pos-rawcounts        <=  hm2_5i25.0.encoder.02.rawcounts
---
> net z-index-enable    axis.2.index-enable  <=>  hm2_5i25.0.encoder.08.index-enable
> net z-pos-rawcounts        <=  hm2_5i25.0.encoder.08.rawcounts
188,189c200,201
< net z-neg-limit     =>  axis.2.neg-lim-sw-in
< net z-pos-limit     =>  axis.2.pos-lim-sw-in
---
> net both-z     =>  axis.2.neg-lim-sw-in
> net both-z     =>  axis.2.pos-lim-sw-in
205d216
< setp   pid.s.maxerror .0005
280,300c291,295
< #  ---estop signals --- copied from BigJohnT's post on linuxcnc
< loadrt estop_latch
< addf estop-latch.0 servo-thread
< net estop-loopout iocontrol.0.emc-enable-in <= estop-latch.0.ok-out
< net estop-loopin iocontrol.0.user-enable-out => estop-latch.0.ok-in
< net estop-reset iocontrol.0.user-request-enable => estop-latch.0.reset
< ###net remote-estop estop-latch.0.fault-in <=  parport.0.pin-in0-not
< net remote-estop estop-latch.0.fault-in <= hm2_5i25.0.7i77.0.0.input-00-not 
< 
< 
< #  ---original estop signals
< #net estop-out     <=  iocontrol.0.user-enable-out
< #net estop-out     =>  iocontrol.0.emc-enable-in
< 
< #  ---toolchange signals for custom tool changer---
< 
< #net tool-number             <=  iocontrol.0.tool-prep-number
< #net tool-change-request     <=  iocontrol.0.tool-change
< #net tool-change-confirmed   =>  iocontrol.0.tool-changed
< #net tool-prepare-request    <=  iocontrol.0.tool-prepare
< #net tool-prepare-confirmed  =>  iocontrol.0.tool-prepared
---
> 
> net estop-out     <=  iocontrol.0.user-enable-out
> net estop-ext     =>  iocontrol.0.emc-enable-in
> 
> #  ---manual tool change signals---
303,306c298,302
< net tool-change iocontrol.0.tool-change => hal_manualtoolchange.change
< net tool-changed iocontrol.0.tool-changed <= hal_manualtoolchange.changed
< net tool-number iocontrol.0.tool-prep-number => hal_manualtoolchange.number
< net tool-prepare-loopback iocontrol.0.tool-prepare => iocontrol.0.tool-prepared
---
> net tool-change-request     iocontrol.0.tool-change       =>  hal_manualtoolchange.change
> net tool-change-confirmed   iocontrol.0.tool-changed      <=  hal_manualtoolchange.changed
> net tool-number             iocontrol.0.tool-prep-number  =>  hal_manualtoolchange.number
> net tool-prepare-loopback   iocontrol.0.tool-prepare      =>  iocontrol.0.tool-prepared
>